## Slide 1: The examination of membrane potentials
Department of Physiology
Ivan Srejović
Faculty of Medical Sciences
University of Kragujevac

## Slide 2: Historical background
Beginning with Luigi Galvani’s pioneering work in the 18th century and the work of Emil du Bois-Reymond, Johannes Peter Müller, and Hermann von Helmholtz in the 19th century, the excitability of membranes and cells has always been of major interest for research on the nervous system;
Alan Lloyd Hodgkin and Andrew Huxley revealed the ion channel events of action potentials in 1952 using the voltage-clamp technique and were awarded the Nobel Prize in Physiology and Medicine in 1963 for their outstanding work;
In the late 1970s, Bert Sakmann and Erwin Neher refined the voltage-clamp technique and, for the first time, resolved single ion channel currents across a membrane patch;
They were also honored with the Nobel Prize in Physiology and Medicine in 1991.

## Slide 3: The patch-clamp technique
The patch-clamp technique allows the investigation of a small set or even single ion channels;
A single ion channel conducts around 10 million ions per second, but the current is only a few picoamperes;
Tight seal electrically isolates the membrane patch, which means that all ions flowing through the membrane patch flow into the pipette and are recorded by a chlorided silver wire electrode (acts as a silver chloride (Ag/AgCl) electrode) connected to a highly sensitive electronic amplifier.

## Slide 4: The patch-clamp technique
To prevent alterations in the membrane potential, a compensating current that resembles the current that is flowing through the membrane is generated by the amplifier as a negative feedback mechanism;
The membrane potential of the cell is measured and compared to the command potential;
The membrane potential of the cell is measured and compared to the command potential;
If there are differences between the command potential and the measurement, a current will be injected.

## Slide 5: Patch-clamp configurations
Depending on the research interest, different configurations can be used. In the cell-attached mode, the membrane patch is left intact;
A modification of the cell-attached mode is the loose-patch.
In this case, the pipette is not tightly sealed to the membrane, but is only loosely attached to it;
This mode is often used to record action potentials in neuronal cells;
The most commonly used patch-clamp mode is the whole-cell mode.
To achieve this mode, the membrane patch is disrupted by briefly applying strong suction.
The interior of the pipette becomes continuous with the cytoplasm.
This method is used to record the electrical potentials and currents from the entire cell.
It is also possible to record currents only from a small patch instead of the whole cell (raises the chances of recording single channels).

## Slide 6: Patch-clamp configurations

## Slide 7: Applications of patch clamping
Patch-clamp experiments are used to gather data which can answer a large variety of physiological questions, not only in the field of neuroscience.
Patch-clamp recordings have also become more important for the investigation of ion channels in non-excitable cells.
It is also a very important method for medical research, because many diseases are related to a malfunction of specific ion channels.
In pharmacological research, automated patch clamping is used to screen potent substances for ion-channel modifications.
Patch-clamp recordings can also be combined with live-cell imaging approaches, such as calcium-ion (Ca2+) imaging.
Preparation of acute brain slices
Electrophysiology on acute brain slices
Electrophysiology on cultured cells

## Slide 8
Action potential of cod (Eleginus nawaga) cardiomyocytes –
White Sea Biological Station, Russia