## Slide 1
LUNGS
Nuclear Medicine Scans: Analysis of uptake mechanism and imaging protocols

## Slide 2: V/Q ventilation/perfusion scintigraphy
Pulmonary imaging

## Slide 3
133Xe
127Xe
81mKr
99mTc-aerosol
VENTILATION SCAN
PERFUSION SCAN
99mTc-mikrosphere
99mTc-MAA
20 – 40 µm
Er (7µm)
bronchus
Alveolar wall
Pulmonary vessel (8,2 µм)
Pulmonary imaging

## Slide 4: PERFUSION SCINTIGRAPHY
Microembolization of precapillarie vessels (1/1000) with particles whose diameter is larger (20-50μ) than the diameter of pulmonary capillaries (8.2μ).
Radiopharmaceuticals:
99mTc-macroaggregated human serum albumin (MAA) (minimum 100000 particles, optimal 200000-600000, caution with D-L shunt!!! T1/2 biol = 2-4h)
99mTc-albumin microspheres
133Xe dissolved in saline for i.v. application

## Slide 5: PA
AP
Upper mediastinum
Right APEX
Cardiac impression
Left APEX
RL
LL
LL
RL
HILUM
Right lateral
ANTERIOR
POSTERIOR
Diaphragm
Left lateral
ANTERIOR
POSTERIOR
Cardiac impression
PERFUSION SCINTIGRAPHY

## Slide 6: VENTILATION SCINTIGRAPHY
133Xe, 127Xe и 81mKr radioactive gases
distal of the obstruction - reduced hypoperfusion "cold fields"
3 phases: "Wash-in, equilibrium and wash-out" scintigrams
1. Ventilation rate of different lung segments
2. Volume of gas distribution
3. Information on prolonged gas retention (COPD)

## Slide 7: VENTILATION SCINTIGRAPHY
Technegas
Pertehnegas
Radioactive aerosols produced in a commercial generator and used for lung scintigraphy. The aerosols are produced by first evaporating to dryness standard technetium-99m generator eluate (99mTcO4) in a graphite crucible (the simmer stage) and then heating this to 2500 degrees C (the "burn" stage).
Patients inhale the Technegas via tubing and a mouthpiece, with particles lodging within the peripheral lungs.
Technegas has been reported to have better penetration of the peripheral lungs and less clumping of tracer in the central airways when compared to aerosolized Tc-99m DTPA. Technegas will remain lodged in the lungs as the isotope decays, with no absorption via the capillary beds or renal excretion.
0,02-0,2um
100% Ar
0,02-0,2um
95% Ar + 5% O2

## Slide 8: VENTILATION SCINTIGRAPHY
133Xe, 80 keV, 5,3 days Т1/2,
WASH-IN
EQUILIBRIUM
WASH-OUT
0 -15”
15 - 30”
30 - 45”
45 - 60”
60 - 120”
120 - 180”
0 -10”
10 - 20”
20 - 30”
30 - 45”
45 - 60”
60 - 75”

## Slide 9: VENTILATION SCINTIGRAPHY
Aerosols 99mTc-diethylenetriaminepentaacetate (DTPA)
An aerosol of 99mTc-DTPA was produced using pressurised air. The jet nebuliser produces an aerosol with a median aerodynamic diameter of less than 1 μm.
Patients are sitting in front of a gamma camera and inhaled the aerosol during normal tidal breathing through a mouthpiece with a one way valve and noseclip in place.
Airway obstruction „hot spot“, distal of the obsrtuction “cold spost”

## Slide 10: VENTILATION SCINTIGRAPHY
Normal scan
AP
PA
RPO
LPO
99mTc-DTPA
Upper mediastinum
Right APEX
Cardiac impression
Left APEX
LL
RL
HILUM
ANTERIOR
POSTERIOR
Diaphragm
ANTERIOR
POSTERIOR

## Slide 11
P
V
V/Q ventilation/perfusion scintigraphy
Normal scan
P
V

## Slide 12: ANATOMY AND PHYSIOLOGY OF THE LUNGS
For the interpretation of the scan its an important knowledge of pulmonary vascular segmental anatomy which almost completely follows bronchopulmonary segmental anatomy except in the apical parts of the lungs

## Slide 13: V/Q ventilation/perfusion scintigraphy
Indications:
pulmonary embolism,
F/U pulmonary embolism after anti-coagulant therapy,
CTEPH (Chronic thromboembolic pulmonary hypertension)
perfusion change secondary to lung tumor,
pre-operative evaluation for pneumonectomy, post-operative F/U…

## Slide 14: PULMONARY EMBOLISM
A pulmonary embolism is a sudden blockage in your pulmonary arteries, the blood vessels that send blood to your lungs. It usually happens when a blood clot in the deep veins in leg breaks off and travels to your lungs
Clinical symptoms: chest pain, dyspnea, hemoptysis
Lab tests:
D-dimer, gass analysis
ЕCG – sinus tachycardia,
С1Q3Т3, РБББ, P pulmonale
Imaging :
RTG
MDCT
V/Q scan
Angiography

## Slide 15
PULMONARY EMBOLISM
Notes: Being a radiation- and contrast medium-sparing procedure, the V/Q scan may preferentially be applied in outpatients with low clinical probability and a normal chest X-ray, in young (particularly female) patients, in pregnancy, in patients with history of contrast medium-induced anaphylaxis and strong allergic history, in severe renal failure, and in patients with myeloma and araproteinaemia.
Performing only a perfusion scan is acceptable in patients with a normal chest X-ray; any perfusion defect in this situation will be considered to be a mismatch. The high frequency of non-diagnostic intermediate probability scans has been a cause for criticism, because they indicate the necessity for further diagnostic testing. Various strategies to overcome this problem have been proposed,notably the incorporation of clinical probability.
Recent studies suggest that data SPECT imaging, with or without low-dose CT may reduce the frequency of non-diagnostic scans

## Slide 16: “V/P Mismatch”
Ventilation ≥
Perfusion
PULMONARY EMBOLISM

## Slide 17
1 segment
superior
RPO
PULMONARY EMBOLISM
Ventilation
Perfusion

## Slide 18
Copyright © Society of Nuclear Medicine and Molecular Imaging
PULMONARY EMBOLISM
Notes: Representative SPECT/CT images in patient with multiple PE. Several mismatched defects are evident (arrows). CT shows no underlying structural abnormalities.

## Slide 19
Parenchymal lung disease
“V/P Match”
Ventilation =
Perfusion

## Slide 20
P
V
Rtg
Previous tuberculosis can lead to of significantly larger P defects in relation to the X-ray findings.
Parenchymal lung disease

## Slide 22
PISAPED ctiteria

## Slide 23
Notes: Being a radiation- and contrast medium-sparing procedure, the V/Q scan may preferentially be applied in outpatients with low clinical probability and a normal chest X-ray, in young (particularly female) patients, in pregnancy, in patients with history of contrast medium-induced anaphylaxis and strong allergic history, in severe renal failure, and in patients with myeloma and araproteinaemia.
Performing only a perfusion scan is acceptable in patients with a normal chest X-ray; any perfusion defect in this situation will be considered to be a mismatch. The high frequency of non-diagnostic intermediate probability scans has been a cause for criticism, because they indicate the necessity for further diagnostic testing. Various strategies to overcome this problem have been proposed,notably the incorporation of clinical probability.
Recent studies suggest that data SPECT imaging, with or without low-dose CT may reduce the frequency of non-diagnostic scans

## Slide 25: V/Q scan in pregnancy

## Slide 26
__________________________________________________________
Test Estimated radiation
uGy mSv
……………………………………………………………………………………………...
Chest radiography <10 0.01
Perfusion lung scan with technetium 60–120 0.06–012
99m-labelled albumin
V/Q scan 200 0.2
CT angiography
First trimester 3–20 0.003–0.02
Second trimester 8–77 0.008–0.08
Third trimester 51–130 0.051–0.13
Pulmonary angiography by femoral 2210–3740 2.2–3.7
access
The Task Force for the Diagnosis and Management of Acute Pulmonary Embolism for the European Society of Cardiology European Heart Journal 2008
V/Q scan in pregnancy

## Slide 27
Chronic thromboembolic pulmonary hypertension (CTEPH)

## Slide 28
Chronic thromboembolic pulmonary hypertension (CTEPH)

## Slide 29: PULMONARY CARCINOMA
Lung cancer is a disease of great sociomedical importance, due to its high incidence and mortality. Etiologically, it is associated with the inhalation of tobacco smoke. Previously, it occurred much more often in men, but the percentage of affected women is increasing.

## Slide 30
Small cell carcinoma produces regional and distant metastases very early, and the chance of a radical cure is very small. Most often, no surgery is performed.
Other histological types are less malignant and in less advanced cases, radical surgery and adjuvant chemotherapy and radiotherapy can be successful.
Reliable diagnostics are needed to clearly distinguish patients with good chances of recovery from those with poor ones.

## Slide 31
Glocose uptake [18F]FDG NSCLC
NETs SSTR [111In]Octreotate SCLC [68Ga] DOTATOC
Protein syntesis [11C]methionine
Phospholypids syntesis [11C]Choline
Cell proliferation [18F]FLT
Cell hypoxia [18F]FMISO
[18F]FAZA
[64Cu]ATSM
Apoptosis [18F]Annexin V
Angiogenesis [18F]NGR-peptide
IMAGING LUNG CANCER

## Slide 32
Fluorodeoxyglucose (FDG) is phosphorylated to FDG-6-PO4 by hexokinase. Since the activity of glucose-6-phosphatase is negligible, FDG-6-phosphate is essentially trapped in tumor cells.
Unfortunately it is also trapped in activated macrophages.
18F (18FDG)

## Slide 33
Diagnosis and “grading” of malignant disease
Definition of disease extent: staging and restaging
Identification and localisation of disease foci unknown primary (paraneoplastic syndromes)
Evaluation and monitoring of response to therapy
Identification of recurrent disease in comparison with “raising” tumour markers and anatomic/structural changes (CT and MR)
Guide for biopsy
Therapy guidance and “management”
PET with FDG in ONCOLOGY LUNG CANCER

## Slide 34: Evaluation of Solitary Pulmonary Nodule
Large numbers of SPNs detected, ~10 for every case of cancer.
    Lung biopsies: significant morbidities & costs.
    CT: Limited ability to characterize tissue*.
  * Fletcher JW, Kymes SM, Gould M, et al. A comparison of the diagnostic accuracy of 18F-FDG PET and CT in the characterization of solitary pulmonary nodules. J Nucl Med 2008; 49:179-185.

## Slide 35: Evaluation of Solitary Pulmonary Nodule
Sn 97% ( 83-100%) Sp 78% ( 52-100%)
False negative (SPN<5mm)
Meta analiza, Dwamena et.al., Radiology, 2000: 513-536
Application of FDG-PET in patients with SPN reduces unnecessary resections by 20%

## Slide 38: Staging” NSCLC
The primary goal of pre-treatment staging is to determine the extent of
disease so that management and prognostication can be done.
Staging is based on:
Tumor Size
Location
Nodal Involvement
Presence/Absence
of Metastasis
Precise Primary Tumor
and Nodal Staging
CT
Sn 20-86% (65%)
Sp 43-90% (80%)
Acc 52-79% (75%)
Dwamena et.al., Radiology, 2000: 513-536
FDG-PET
Sn 67-100% (89%)
Sp 79-100% (92%)
Acc 78-100% (90%)

## Slide 41
TNM 2009
Lababede O, Chest 2011; 139: 183-189

## Slide 42
Detterbeck F, Chest 2009; 136: 260-271
TNM

## Slide 43: surgically resectable.
not surgically resectable
potentialy surgically resectable with CHT

## Slide 44: LIMITATIONS OF CT
Limited ability to differentiate benign from malignant lesions
Limited usefulness in the detection of chest wall and mediastinal invasion
  Sensitivity & Specificity = 50-70%1
Several meta-analysis reported low sensitivity and specificity of CT for mediastinal LN involvement:
  Sensitivity = 50-65% 2
  Specificity = 65-85%
Vesselle H et al. J Thorac Cardiovasc Surg 2002; 124: 511-519
Birim O et al. Ann Thorac Surg 2005; 79: 375-381

## Slide 45: PET/CT NSCLC N-Staging
PET changes N Staging u 21% of patients planning for surgery (Beadsmoore et al. Eur J Radiol 2003)
CT
PET is more accurate than CT for N-Staging NSCLC.
(Baum et al. Q J Nucl Med Mol Imaging 2004)
PET
45

## Slide 46: T2-N0-M0: Stage IB

## Slide 47
Stage IIIA: T3, N2, M0

## Slide 48
Stage IV: T3, N0, M1b

## Slide 49
Stage IV: T3, N0, M1b

## Slide 50: Small Cell Lung Cancer Neuroendocrine aggressive tumor
Two stage classification:
Limited: tumor confined to unilateral chest
Treatment: Chemotherapy and radiation Extensive: Contralateral or distant disease
Treatment: Chemotherapy + PPRT
Change of management due to FDG PET: 8-29%
Blum R et al. Am J Clin Oncol 2004;27:164-171.
Bradley JD et al. J Clin Oncol 2004;22:3248-3254.

## Slide 51
For neuroendocrine lung tumors
  18F-DOPA
  68Ga-DOTA TOC/TATE/NOC
For dedifferentiation of neuroendocrine lung tumors
  18F-FDG

## Slide 52: small cell lung cancer- SCLC
SSTR imaaging (Octreoscan®)
well-differentiated NETs express somatostatin receptors, so this method can not only detect NETs and their metastases, but also opens up the possibility of therapeutic application of somatostatin analogs

## Slide 53: small cell lung cancer- SCLC
18FDG (-)
68Ga-Dotatoc (+)

## Slide 54: CONCLUSION
Integrated PET/CT provides:
  More precise staging than all the other imaging techniques
  Allows better selection of patients for new modalities of treatment
  Helps in re-staging after induction therapy
  It is cost-effective
  Precise delineation – EBRT Planning
  Helps in follow up evaluation by differentiating Residual or recurrent tumor from Post-treatment scarring