## Slide 1: The Radiopharmacy and Radiopharmaceuticals

## Slide 2: Nuclear medicine and radiotracer
Nuclear medicine, in the simplest terms, is the medical specialty based on examining the regional chemistry of the living human body.
In the 1920s, Georg De Hevesy coined the term “radioindicator” (radiotracer) and introduced the “tracer principle” to the biomedical sciences.
One of the most important characteristics of a true tracer is the ability to study the components of a homeostatic system without disturbing their function.
Notes: <number>

## Slide 3
Radioactivity is a property of atomic nuclei and may be defined as the spontaneous transformation of a structurally unstable nucleus to a structurally more stable nucleus, with the emission of energy in the form of ionizing radiation.
A nucleus not in its stable state will adjust itself until it is stable either by ejecting portions of its nucleus or by emitting energy in the form of photons (gamma rays). This process is referred to as radioactive decay.
Two features largely determine the structural stability of a nucleus: the size (i.e., atomic number, Z) and the neutron-to-proton (N-to-Z) ratio.
Notes: All large nuclei (i.e., Z >80) are structurally unstable and therefore radioactive. For nuclei with an atomic number Z < 80, structural stability depends on the neutron-to-proton (N-to-Z) ratio.
For small nuclei (i.e., Z <20), stability is achieved for nuclei having an equal number of neutrons and protons, that is, an N-to-Z ratio of 1.
For nuclei 20 <Z <80 stability is achieved for nuclei having three neutrons for every two protons or an N-to-Z ratio of 1.5.
<number>

## Slide 4: Definition of a Radiopharmaceutical
A radiopharmaceutical is a radioactive drug used for diagnosis or therapy in a tracer quantity, masses so small that they do not produce pharmacologic effects,
It is composed of two parts : a radionuclide and a pharmaceutical
Notes: Although the term radiopharmaceutical is most commonly used, other terms such as radiotracer, radiodiagnostic agent, and tracer are used as well.
<number>

## Slide 5: Definition of a Radiopharmaceutical
The usefulness of a radiopharmaceutical depends on characteristics of radionuclide and ligand (vector molecule)
Ligand: The properties are primarily responsible for dictating how the product will behave in the body. Ligand is chosen on the basis of its preferential localization in a given organ or its participation in the physiologic function of the organ.
Notes: Then a suitable radionuclide is tagged onto the chosen pharmaceutical such that after administration of the radiopharmaceutical, radiations emitted from it are detected by a radiation detector.
<number>

## Slide 6: Ideal Properties of Diagnostic Radiopharmaceutical
Decay mode: Electron capture or isomeric transition from metastable states; gamma emission , without particulate radiation;
Photon energy: 100 - 200 keV is ideal.
Short Effective Half-Life: Effective Half-Life (Te) in any biologic system, the loss of a radiopharmaceutical is due to both the physical decay of the radionuclide and the biologic elimination of the radiopharmaceutical. The physical half-life (Tp) is independent of any physicochemical condition and is characteristic for a given radionuclide.
Biologic half-life (Tb): Radiopharmaceuticals administered to humans disappear from the biological system through fecal or urinary excretion, perspiration, or other mechanisms. Thus, every radiopharmaceutical has a biologic half-life.
1/TE = 1/TB + 1/TP or TE =(TB TP)/ (TB + TP)
Notes: The gamma emission has to be strong enough to easily penetrate the body barrier and also has to be well detectable by the common SPECT camera systems.
A radionuclide decays with a definite half-life, which is called the physical half-life
<100 keV = tissue absorption and scatter (decreases resolution). >200 keV there is low detection efficiency. (decreases sensitivity )
Optimal 1 to 1.5 times of the imaging time.
<number>

## Slide 7: Ideal Properties of Diagnostic Radiopharmaceutical
Easy Availability: The radiopharmaceutical should be easily produced, inexpensive, and readily available in any nuclear medicine facility
Chemical properties: Can be compounded into different chemical forms.
High Target-to-Non-target Activity Ratio: it is desirable that the radiopharmaceutical be localized preferentially in the organ under study, while maintaining minimum uptake in the normal tissue
The stability of a labeled compound is one of the major concerns in labeling chemistry. It must be stable both in vitro and in vivo.
An ideal radiopharmaceutical should have all the above characteristics to provide maximum efficacy in the diagnosis of diseases and a minimum radiation dose to the patient.
However, it is difficult for a given radiopharmaceutical to meet all these criteria and the one of choice is the best of many compromises.

## Slide 8: Diagnostic vs. therapeutic isotope
In nuclear medicine nearly 95% of the radiopharmaceuticals are used for diagnostic purposes, while the rest are used for therapeutic treatment.

## Slide 9: Factors Influencing the Distribution and Localization of Radiopharmaceuticals
  Protein binding is greatly influenced by a number of factors, such as the charge on the radiopharmaceutical molecule, the pH, the nature of protein, and the concentration of anions in plasma.
  Protein binding affects the tissue distribution and plasma clearance of a radiopharmaceutical and its uptake by the organ of interest
Notes: Almost all drugs, radioactive or not, bind to plasma proteins to variable degrees. The primary candidate for this type of binding is albumin, although many compounds specifically bind to globulin and other proteins as well.
Indium, gallium, and many metallic ions bind firmly to transferrin in plasma.
<number>

## Slide 10: Factors Influencing the Distribution and Localization of Radiopharmaceuticals
Notes: lipid solubility of a radiopharmaceutical is a determining factor in its localization in an organ; the cell membrane is primarily composed of phospholipids, and unless the RF is lipid soluble, it will hardly diffuse through the cell membrane.
The higher the lipid solubility of a radiopharmaceutical, the greater the diffusion through the cell membrane and hence the greater its localization in the organ.
Protein binding reduces the lipid solubility of a radiopharmaceutical. Ionized drugs are less lipid soluble, whereas nonpolar drugs are highly soluble in lipids and hence easily diffuse through cell membranes.
<number>

## Slide 11
Particulate emission: α, β– or Auger electron emitters with a physical half-life in the range of several hours to about 10 days, a small amount of accompanying γ -emission is advantageous to determine the radioactivity distribution in the body and for dosimetry.
Energy: medium/high (>1 MeV)
Effective Half-life: 5-20 days
The higher the linear energy transfer (LET) of the emitter, the higher will be the effect on the targeted tissue per decay
Target-to-Non target Ratio
Easy Availability
Ideal Therapeutic Radiopharmaceuticals
Notes: In order to achieve a maximum therapeutic effect in the targeted tissue, the radioisotopes used in therapy include α, β– or Auger electron emitters with a physical half-life in the range of several hours to about 10 days
a small amount of accompanying γ -emission (~10% of disintegrations; γ energy ~150 keV) is advantageous to determine the radioactivity distribution in the body and for dosimetry.
The choice of the radionuclide depends on the site of targeting at the cellular level and the effective range of the particle emission.
Thus therapeutic radiopharmaceuticals labeled with Auger electron emitters should be able to target the cell nucleus and those labeled with α-emitters should be at least internalized into the cell, while compounds labeled with β– emitters may be allowed for targeting the cell surface or for just getting into close proximity to the targeted tissue.
the higher the linear energy transfer (LET) of the emitter, the higher will be the effect on the targeted tissue per decay
The uptake mechanisms of therapeutic radiopharmaceuticals are the same as with diagnostic.
<number>

## Slide 12: Production Modes
According to their production modes, radionuclides can be divided into three groups:

## Slide 13: Reactors
Radionuclides for nuclear medicine are also produced in nuclear reactors. Some examples include 131I, 133Xe, and 99Mo.
It is composed of fuel rods that contain large atoms (typically uranium- 235, uranium-238, or plutonium-239) that are inherently unstable. These atoms undergo fission. Two or three neutrons and approximately 200MeV of heat energy are emitted during fission.
If this chain reaction were to grow unchecked, the mass would explode.
To maintain control, cadmium control rods are inserted to absorb the neutrons in the reactor.
Notes: These neutrons leave the nucleus with moderately high kinetic energy and are referred to as fast neutrons. The neutrons are slowed with a moderator such as graphite, water, or heavy water. These “very slow” or thermal neutrons, and to a lesser extent the fast neutrons, in turn impact other fissionable atoms causing their fission, and so forth. If this chain reaction were to grow unchecked, the mass would explode.
<number>

## Slide 14: Reactor Nuclides
(n, γ ) reaction produce neutron-rich isotopes, thermal neutrons will react with stable isotopes deposited inside a reaction chamber in defined areas of the nuclear reactor. This will preferably lead to β –-emitters. Isotopes produced like this are of relatively low specific activity, as the produced isotope is of the same element as the target. Thus the produced isotope cannot be chemically separated from the target isotope.
(n, p) reaction: may occur in regions of the nuclear reactor where fast neutrons dominate. In this case, the mass of the produced isotope will not change. However, by eliminating a proton from the target isotope a change in the element (one unit lower) will occur.
Notes: Thermal neutrons will react with stable isotopes deposited inside a reaction chamber in defined areas of the nuclear reactor. Neutrons will penetrate through the target and react with the target material using the (n, γ ) nuclear reaction to produce neutron-rich isotopes. This will preferably lead to β –-emitters. Isotopes produced like this are of relatively low specific activity as the produced isotope is of the same element as the target. Thus the produced isotope cannot be chemically separated from the target isotope.
In different regions of the nuclear reactor where fast neutrons dominate, a different nuclear reaction – the (n, p) reaction –may occur. In this case, the mass of the produced isotope will not change. However, by eliminating a proton from the target isotope a change in the element (one unit lower)will occur.
<number>

## Slide 15: Cyclotron Nuclides
Since a high energy beam of positively charged particles is required to produce proton rich radionuclides, accelerators have been developed to generate a well defined, high energy beam of charged particles with high beam intensity.
Because acceleratable particles are of a charged nature, typical cyclotron produced isotopes are neutron deficient. They are produced by irradiation of stable target compounds with charged particles like protons (p), deuterons (d) or helium nuclei.
Because of the neutron deficient nature of the produced isotopes, they tend to stabilize by electron capture (EC) or by positron emission ( β +). These decay modes are particularly useful for nuclear medicine purposes and they are thus useful diagnostic isotopes.
Notes: Since a high energy beam of positively charged particles is required to produce proton rich radionuclides, accelerators have been developed to generate a well defined, high energy beam of charged particles with high beam intensity. The cyclotron or the medical cyclotron is the most widely used particle accelerator to produce high energy protons and deuterons for the production of positron emitting radionuclides.
The cyclotron consists of three major components:
an electromagnet with a field strength of 1.5–2.0 tesla,
a pair of semicircular hollow copper electrodes, called “dees” located between the poles of the magnet,
ion source capable of generating high intensity negative ions.
The entire structure of the cyclotron is kept under high vacuum (up to 10–7 torr).
Traditionally, the cyclotrons were designed to accelerate positive ions (H+ and 2H+). The first cyclotron designed
to accelerate negative ions, hydrogen or deuterium atoms with two electrons in the K-shell (H– and
2H–) was built in 1966. Since the 1980s all the commercial
medical cyclotrons have been basically negative ion cyclotrons. One of most important advantages of the
negative ion cyclotron is the elimination of a complex beam extraction system. As
<number>

## Slide 16: Cyclotron Nuclides
The cyclotron consists of three major components:
an electromagnet with a field strength of 1.5–2.0 tesla,
a pair of semicircular hollow copper electrodes, called “dees” located between the poles of the magnet,
ion source capable of generating high intensity negative ions.
The entire structure of the cyclotron is kept under high vacuum.
Notes: circular devices in which charged particles (protons and α particles) are accelerated in a spiral path within a vacuum. The power supply provides a rapidly alternating voltage across the Dees (the two halves of the circle). This produces a rapidly alternating electric field between the Dees that accelerates the particles, which quickly acquire high kinetic energies. They spiral outward under the influence of the magnetic field until they have sufficient velocity and are deflected into a target.
A deflector is used to direct the particles out through a window of the cyclotron into a target. Some of the particles and kinetic energy from these particles are incorporated into the nuclei of the atoms of the target.
<number>

## Slide 17: Cyclotron Nuclides
Because acceleratable particles are of a charged nature, typical cyclotron produced isotopes are neutron deficient. They are produced by irradiation of stable target compounds with charged particles like protons (p), deuterons (d) or helium nuclei.
Because of the neutron deficient nature of the produced isotopes, they tend to stabilize by electron capture (EC) or by positron emission ( β +). These decay modes are particularly useful for nuclear medicine purposes and they are thus useful diagnostic isotopes.

## Slide 18: PET Radionuclides
the organic positron emitters such as 11C,13N, 15O and 18F.
The physical half-life of most of these positron emitters is relatively short (<2 h) and as a result the theoretical specific activity (SA) is very high.
The basic principle of PET imaging technique is based on the coincident detection of annihilation photons produced by the interaction of positron with an electron.
PET imaging

## Slide 19: PET Radiopharmaceuticals: Mechanisms of Cellular Uptake and Localization
Compared to SPECT, the PET technique has the unique advantage of developing radiopharmaceuticals as diagnostic radiotracers or molecular imaging probes to detect and quantitate the function of an organ or a unique biochemical process in a specific tissue.
PET radiopharmaceuticals can be generally classified based on their ability to image a specific biochemical process or based on their unique mechanism of localization in a specific organ/tissue of interest .
Notes: It is an absolute requirement that these imaging probes be designed in such a way that the study can be performed without disturbing the biochemical process under investigation.
<number>

## Slide 20: Molybdenum/Technetium Generators
All radionuclide generators work on the principle that a relatively long-lived “parent” radionuclide decays to produce a “daughter” radionuclide, where the chemical nature of parent and daughter are quite different. This difference allows separation of the daughter from the parent.
The 99Mo/99mTc generator consists of 99Mo absorbed onto an alumina filled column. The 99Mo decays to its daughter radionuclide 99mTc

## Slide 21
99mTc is removed from the column as sodium pertechnetate, Na99mTcO4, by drawing a solution of sodium chloride (NaCl) 0.9% through the column. This process is known as eluting the generator and gives a sterile solution of sodium pertechnetate (the eluate)
Rachel A., Essentials of nuclear medicine physics. III
Notes: The 99mTc (daughter) is “milked” (eluted) by drawing sterile saline through the column into the vacuum vial. The parent 99Mo(small grey circles) remains on the column, but the daughter 99mTc (white circles) is washed away in the saline.
Typically the molybdenum-99 is bound strongly to the aluminum oxide matrix. The radioactive daughter nuclide 99mTc will be formed in the chemical form of pertechnetate (99mTcO-4), which is weakly bound and thus easily eluted.
A generator is frequently called a cow, the elution of the daughter nuclide is referred to as milking, and the surrounding lead is called a pig, a term used for any crude cast-metal container. Generators come in small sizes for use in a standard nuclear medicine department or in larger sizes for use in central laboratories.
<number>

## Slide 22: Technetium-99m
decays with a half-life of 6.0 h by isomeric transition to 99mTc, emitting a single photon with an energy of 141 keV.
The rich complex chemistry of technetium allows incorporation of the radioisotope into a wide variety of ligands stabilizing the radionuclide at different oxidation states.
In order to form Tc-99m-labeled organic molecules it is necessary to reduce the pertechnetate anion to a lower oxidation state. A variety of reducing agents might be used; however, stannous(II) ions are used in most cases.
Notes: This energy almost ideally meets the sensitivity maximum of SPECT camera systems.
<number>

## Slide 23: Preparation of a Technetium-99m labeled radiopharmaceutical
Tc-99m as sodium Pertechnetate is added to the reaction vial
Tc-99m radiopharmaceutical is ready for dispensing
The patient dose is withdrawn from the vial
Each dose is measured in the dose calibrator before it dispensed
Notes: radiopharmaceuticals are produced by combining the radionuclide with a number of non-active sterile compounds contained within a sealed sterile vial (kit).
A kit has been defined as a “pre-packed set of sterile ingredients designed for the preparation of a specific radiopharmaceutical”
Most commonly the ingredients are: ligands, stannous ions (Sn2+) which are present as a reducing agent, other compounds that act as stabilizers, buffers, antioxidants, or bactericides.
the simple addition of pertechnetate into the vial followed by shaking to dissolve the contents. This is then sometimes followed by a short incubation period at room temperature, although heating is necessary with some kits (e.g. 99mTc-MAG3 and 99mTc-sestamibi
<number>

## Slide 24: Characteristics of Commonly Used Generators
Notes: examples of radionuclide generator systems for clinical applications which provide daughter radioisotopes for diagnostic applications
The parent isotope Ge-68 has a half-life of 270.95 days and can be easily delivered to hospitals as a generator, where it can be used as the source of Ga-68 for at least 1 year
<number>

## Slide 25: Radiopharmaceuticals classification on their ability to image a specific biochemical process
Perfusion Agents (Myocardial, Brain , Lung Perfusion)
Lung Ventilation Imaging Agents
  Metabolism Agents (Glucose, Amino Acid, Nucleosides Metabolism, Hypoxia Imaging)
  Peptides and Proteins (Somatostatin Receptor Tracers, Annexin V)
  Monoclonal Antibodies
  Neurotransmitter Receptor and Transporter Tracers (Benzodiazepine, Serotonergic (5-HT), Dopaminergic Receptor Tracers, Dopamine Transporter (DAT), Norepinephrine Transporter (NET)
  Amyloid Imaging
  Cell Labeling

## Slide 26: IDEAL GENERATOR SYSTEMS
1. If intended for clinical use, the output of the generator must be sterile and pyrogen-free.
2. The chemical properties of the daughter must be different than those of the parent to permit separation of daughter from parent.
3. Generator should be eluted with 0.9% saline solution and should involve no violent chemical reactions. Human intervention should be minimal to minimize radiation dose.
4. Daughter isotope should be short-lived gamma-emitting nuclide (physical half-life = hrs-days)
5. Physical half-life of parent should be short enough so daughter regrowth after elution is rapid, but long enough for practicality.
6. Daughter chemistry should be suitable for preparation of a wide variety of compounds
7. Inexpensive, effective shielding of generator, minimizing radiation dose to those using it.

## Slide 27
Radiopharmaceutical agents exhibit a huge range of physical and chemical properties and may be classified into eight different categories | 
Radiolabeled particles | 99mTc-MAA
Radiolabeled gases | 133Xe, 127Xe, 81mKr 99mTc-Technegas
Radiolabeled chelates | 99mTc-MDP, HDP 99mTc-DTPA 99mTc-MAG3
Radiotracers as ions | 99mTc-pertechnetate (TcO-4)
Radiolabeled cells | 99mTC-RBC, 111In-WBC
Receptor binding radiotracers | 111In-pentetreotide, Octreoscan
Radiolabeled monoclonal antibodies | 111In-antimyosin 111In-Prostascint
Radiolabeled metabolic substrates | 18F-Fluorodeoxyglucose, 11C-choline

## Slide 28
The pharmacokinetics, biodistribution, and metabolism of the radiopharmaceutical are very important to understanding
the mechanisms of radiopharmaceutical localization in the organ or tissue of interest.
The mechanisms of radiopharmaceutical localization may be substrate-nonspecific (not participating in any specific biochemical reaction) or substrate specific (participating in a specific biochemical reaction), depending upon the chemistry of the molecule. Many radiopharmaceuticals were designed to take advantage of the pathophysiology in order to increase the specificity of the nuclear medicine imaging techniques.

## Slide 29: Mechanisms of Radiopharmaceutical Localization
Isotope Dilution (51Cr-RBCs, 125I-HSA)
Physicochemical Adsorption (99mTc-labeled phosphonates)
Capillary Blockade (99mTc-MAA)
Cellular Migration and Sequestration (111In-oxine- or 99mTc-HMPAO- leukocytes)
Simple Diffusion (133Xe, 127Xe, 81mKr) inert lipophilic gases,
Diffusion and Intracellular Metabolism/Binding (99mTc-HMPAO, 99mTc-ECD)
Diffusion and Mitochondrial Binding –(99mTc-sestamibi)
Facilitated Diffusion-18F-fluorodeoxyglucose (FDG)
Active Transport-Radioiodide and 99mTc-Pertechnetate Anions.
Phagocytosis-99mTc-sulfur colloid

## Slide 30: What happens when 99mTcO4- is administered IV?
when 99mTcO4- is administered IV 100% of the dose immediately enters the blood stream. Once in the vascular compartment, 99mTcO4- level begin to drop. Physiologically 70 to 80% of the initial dose is partially bound to the RBC. Free 99mTcO4- passes into the interstitial space.
As the rate of free Tech drops, the partially bound 99mTcO4- breaks away from the RBC, becomes free, and then it might enter the interstitial space.
Pertechnetate will also concentrate in the following organs: stomach, salivary glands, thyroid, bowel, mucous membranes, choroids plexus.
Notes: three main tissue types accumulate 99mTc pertechnetate: the thyroid, the stomach, and the salivary glands. High NIS gene expression levels have been detected in these three organs
<number>

## Slide 31: Quality Assurance of Radiopharmaceuticals
The radiopharmaceuticals are formulated as sterile, apyrogenic injections and are intended for administration to patients for a diagnostic or therapeutic purpose. These injections have to comply with the same standards of safety and efficacy as conventional pharmaceuticals.
Analytical tests to check radionuclidic, radiochemical, and chemical purity must be carried out routinely. For injection, the radiopharmaceutical should be in aqueous solution at a pH compatible with blood pH (7.4). The ionic strength and osmolality of the agent should also be appropriate for blood.
Notes: although some results are only obtained retrospectively.
This especially applies to the routine sterility testing carried out on parenteral radiopharmaceuticals.
<number>

## Slide 32: Quality Assurance of Radiopharmaceuticals
Notes: <number>

## Slide 33: Quality Assurance of Radiopharmaceuticals
1. Physicochemical Tests
Physical characteristics-inspect the color, size and state of radiopharmaceutical
Colloidal or aggregated RF: size checked with hemocytometer under a light microscope
99mTc-labeled colloid: for visualization of the reticuloendothelial system： 10nm -1 μm
99mTc-MAA，99mTc-label albumin microsphere： 10 -90μm (>150 μm → pulmonary arterial blockade → embolism; smaller than 10 μm → localize in the reticuloendothelial system)
pH: Ideal pH radiopharmaceutical should be7.4 ( pH of the blood ). However， radiopharmaceutical can vary between 2-9 because of high buffer capacity of blood.
Radionuclidic purity, Radiochemical purity
2.Biological Tests (Sterility test, Apyrogenicity test)

## Slide 34: Radionuclidic Purity
the ratio, expressed as a percentage, of the radioactivity of the radionuclide concerned to the total radioactivity of the source. Radionuclides used medicinally are of a high radionuclidic purity (>95%).
99Mo-99mTc generator: There is the possibility of accidental elution of the parent 99Mo during elution of the generator and a limit test for the 99Mo should be performed. Acceptable limits of contaminants is less than 0.15 µCi per 1 mCi of 99mTc
Radionuclidic purity is determined by measuring the half-live and characteristic radiation emitted by individual radionuclides.
Notes: 99Mo breakthrough from the alumina column.
<number>

## Slide 35: Radiochemical Purity
Radiochemical purity (RCP) may be defined as "the proportion of the total radioactivity in the sample which is present as the desired radiolabelled species“.
For example free 99mTcO4 and hydrolyzed 99mTc in 99mTc labeled complexes are the main radiochemical impurities for 99mTc-based radiopharmaceuticals
For 99mTc radiopharmaceuticals, RCP may be measured by chromatographic means, for example using planar chromatography, electrophoresis, and high performance liquid chromatography (HPLC).
Notes: To determine RCP it is first necessary to separate the various radiochemical forms present in the radiopharmaceutical. Although for reduction of this trace amount of 99mTc only an equivalent amount of Sn2+is needed, 1000 to 1 million times more of the latter is added to the preparation in order to ensure complete reduction.
Radiochemical impurities have various reasons including
decomposition due to the action of solvent, change in
temperature or pH, light, presence of oxidizing or
reducing agents, incomplete reaction, and radiolysis. For
example free 99mTcO4 and hydrolyzed 99mTc in 99mTclabeled complexes (complexes of 99mTc with co-ligand or
transfer ligand) are the main radiochemical impurities
for 99mTc-based radiopharmaceuticals
<number>

## Slide 36: Chemical Purity
for sodium pertechnetate (99mTc) injection - a limit test for the aluminum (Al3+) content of 99mTc eluates. Al3+ may originate from the generator column, being produced during the absorption process of the 99Mo onto the alumina column. It is important to perform this test since Al3+ can affect the stability of some colloidal radiopharmaceuticals.
Notes: Chemical impurities originate in different areas including
the breakdown of the material either before or after
labeling, the inadvertent addition during labeling, and
the undue accompaniment in the preparation of the
compound. For example, aluminum is a chemical
impurity in the 99mTc-eluate and can cause serious
problems including toxicity. The presence of a slight
amount of globulins in the preparation of albumin
aggregates can be considered as chemical impurity. It is
noteworthy that additives, acid, alkali, and buffers are
not considered impurities. The presence of chemical
impurities before radiolabeling may lead to undesirable
labeled species that contribute to adverse effect on
diagnostic test
<number>

## Slide 37: Sterility Assurance, Pyrogen Testing
All preparations intended for parenteral administration must be tested to ensure that they comply with the test for sterility. There are problems, however, in applying this test to 99mTc-RF. Because of their short shelf-life, preparations have to be released prior to the results of the sterility test being known.
Radioactive injections have been shown to support microbial growth, but are far from ideal growth media for long-term microbiological survival.
Even in the absence of radioactivity, generator eluates and reconstituted kits have been shown not to support long-term microbiological growth.
Pyrogens are non-volatile, water-soluble substances that, when injected into the body, cause a rise in temperature

## Slide 38: THANK YOU FOR YOUR ATTENTION!
QUESTIONS