## Slide 1: Radiation therapy techniques Assist. Prof Neda Milosavljević, MD PhD

## Slide 2: Radiotherapy treatment can be perform as:
Brachytherapy (direct or close contact with the radiation source)
External beam radiotherapy (EBRT) (distance beetwen patient and radiation source – ’’source-skin distance, SSD’’).

## Slide 3: Linear accelerators (LINAC)
Kilovoltage x-ray beam therapy– energy < 500 kV.
  typically only used for superficial irradiation of skin cancer and for intra-operative RT (IORT)
Megavoltage X-rays service/unit – energy > 1MV (tipically 4-25 MeV)

## Slide 4: Conventional simulator (fluoroscopic planning machine)

## Slide 5: CT/MRI simulator
Andres A. E. Int J of Radiation Oncology, Biology, Physics. , 2020.

## Slide 6
PRECISE DELIVERY OF THERAPEUTIC RADIATION DOSE IN THE TUMOR TISSUE WITH MINIMAL DAMAGE TO THE SURROUNDING, HEALTHY TISSUE
https://www.omicsonline.org/

## Slide 7
Lee S. 2014.
Evolution of Ionizing Radiation Research

## Slide 8
Perez A. Brady S. 2018.
Conformal radiotherapy (CRT) – the beginnings of the 1960s.
The development of imaging methods (CT, MRI, PET), information technology, modern radiotherapy devices - enabling the development of CRT
Local disease control as a function of delivered dose
Sparing of surrounding, healthy tissues
Dose escalation

## Slide 9: Target volume
Gross Tumor Volume (GTV): the visible part of the tumor (or lymph node), based on the performed clinical-diagnostic procedures. After a surgical treatment (R0 resection) the GTV is not visible.
Clinical Target Volume (CTV): zone of microscopic spread of malignant cells around the visible part of the tumor (CTVt). CTVn is defined around enlarged regional lymph nodes (GTVn), it includes at least the entire anatomical group of lymph nodes to which the involved node belongs.
Planning Target Volume (PTV): the margin that covers the interfractional/intrafractional variations of the CTV position in relation to the geometry of the beam/radiation field, and is caused by: variations in precision, physiological movements.

## Slide 10: Organs at Risk (OAR)
Healthy, surrounding tissues, whose sparing/radiosensitivity is taken into account when creating a radiation plan and carrying out radiotherapy treatment
Additional volume around OAR (PRV - Planning Risk Volume)
A 3D model of the "virtual patient", with a volumetric representation of the geometry of the target volume and the spatial relationships of the target volume and the OAR
Icru 52.

## Slide 15
Initial diagnostic work up (pathology and diagnostics)
Disease staging and disease characterization (e.g. Tumor molecular profile)
Multidisciplinary oncology team – treatment decision
Initial exam, informed decision and patient consent
Positioning and immobilisation
CT/MRI simulation
Radiotherapy planning (radiation oncologist + medical phycisist)
Radiotherapy treatment (with weekly check-up)
Follow up

## Slide 16: POSITIONING AND IMMOBILIZATION

## Slide 17: Three-dimensional conformal radiation, 3D-CRT
Became widely used in the 1970s-80s
CT-guided therapy allows the tumor and normal organs shape and size to be defined in three dimensions
delivery of radiation to a three-dimensional volume using appropriate imaging studies and computer software
Decreases the treatment margins and minimizes the volume of normal tissue receiving a clinically significant radiation dose

## Slide 19
vera2

## Slide 26
TD 64 Gy

## Slide 27: INTENSITY MODULATED RADIATION THERAPY - IMRT
delivers radiation precisely to the target volume while relatively sparing the surrounding normal tissues
inverse planning and computer-controlled radiation and normal tissue avoidance
ability to create multiple targets and multiple avoidance structures, to treat different targets simultaneously to different doses
minimize acute treatment-related toxicity
dose escalation = improved local tumor control
accelerated fractionation scheme - simultaneous integrated boost (SIB)
shortening the overall treatment time

## Slide 30: Volumetric Modulated Arc Therapy, VMAT
highly conformal dose distributions with improved target volume coverage and sparing of normal tissues compared with conventional radiotherapy techniques
reduced treatment delivery time compared with IMRT
allowed the simultaneous variation of three parameters during treatment delivery: gantry rotation speed, treatment aperture shape via movement of MLC leaves and dose rate
OAR sparing?

## Slide 36: OAR constrains
Kang SW, Chung JB, Kim JS, Kim IA, Eom KY, Song C, Lee JW, Kim JY, Suh TS. Optimal planning strategy among various arc arrangements for prostate stereotactic body radiotherapy with volumetric modulated arc therapy technique. Radiol Oncol. 2017 Jan 15;51(1):112-120.
Bladder | V65 < 50% V70 < 35% V75 < 25% V80 < 15%
Sygmoid colon | V50 < 50% V60 < 35% V65 < 25% V70 < 20% V75 < 15%
Rectum | V50 < 50% V60 < 35% V65 < 25% V70 < 20% V75 < 15%
Bowel | V45 < 195 cm3 V15 < 120 cm3
Femur | V40 < 40% V45 < 25% V50< 10%

## Slide 47: IMAGE GUIDED RADIOTHERAPY - IGRT
IGRT allows assessment of geometric accuracy of the “patient model” during treatment.
Provides a method where deviations of anatomy from initial plan are determined and this information is used for updates.
  Interfractional variations
  Positioning
  Organ mobility
  Anatomic variations during treatment
  Intrafractional motion

## Slide 48
RESPIRATORY GATING
improvement in the irradiation of tumor sites affected by respiratory motion such as lung, breast, and liver tumors
decreased radiation related toxicity to organs at risk
  integration of respiratory movements into treatment planning,
  forced shallow breathing with abdominal compression,
  breath-hold techniques,
  respiratory gating techniques,
  tracking techniques

## Slide 49
Hui Z, et al. Int J Radiat Oncol Biol Phys. 2008 Dec 1;72(5):1385-95.

## Slide 50: Stereotactic radiotherapy
high-precision radiotherapy technique that utilises high doses of radiation in a few or single fractions
Stereotactic radiosurgery (SRS); Stereotactic body radiation therapy (SBRT) or stereotactic ablative radiotherapy (SABR)
Numbers of indications
Izvor: Mayo Clinic. SRS.
Radiosurgery.gr

## Slide 51: Stereotactic Body Radiotherapy, SBRT
The use of ablative doses delivered in a small number of fractions, and whose biologically equivalent dose (BED) is >100 Gy.
It prevents tumor repopulation, causes vascular damage, apoptosis of the endothelium, remodeling of the microvasculature, induces an immune response to the tumor.
Abreu C. E. J. bras. pneumol. 2015.

## Slide 52: Proton Therapy
physical properties of a proton beam - modulating the Bragg peak of protons
sparing the surrounding normal tissues - ideal when organ preservation is a priority
Availability and cost of treatment?
Proton Th ILR.2020.

## Slide 53
Izvor: cancernetwork.com

## Slide 54: INTRAOPERATIVE RADIOTHERAPY (IORT)
Precise delivery of a large dose of ionising radiation to the tumour or tumour bed during surgery.
Direct visualisation of the tumour bed and ability to space out the normal tissues from the tumour bed - maximisation of the dose to the tumour/ minimising the dose to normal tissues.
Electrons, low-kV X-rays and HDR brachytherapy
for dose escalation (retroperitoneal sarcoma), EBRT dose de-escalation (paediatric tumours), as sole radiation modality (early breast cancers) and as a re-irradiation modality (recurrent rectal and gynaecological cancers)

## Slide 55: Brachytherapy
By precisely positioning the radioactive source in the immediate vicinity of the tumor (up to 2 cm), it is possible to apply a high dose of radiation to the target volume.
Due to the peripheral dose drop, healthy tissue in the immediate vicinity is spared.
The volume dose is lower than that in EBRT, so the risks for local and systemic radiotoxicity are significantly lower.

## Slide 56
Surface (contact) brachytherapy is performed by bringing the source into close proximity, for the irradiation of tumors localized on the skin and visible mucous membranes.
Intracavitary (intraluminal/endoluminal) - by introducing radioisotopes into natural body cavities using a guide/applicator.
Interstitial brachytherapy where radiation sources are introduced directly into the tumor, through guidesinserted into the tumor tissue or by inserting radioactive grains into the tumor.
MA S. Cancer men. And res. 2019.; Prostate Cancer Brachytherapy. UCLA Health