## Slide 1
Tissue processing for electron microscopy

## Slide 2: Transmission electron microscopy (ТЕМ)
Preparation of tissue for observation on transmission electronic microscope differs from light microscopy.
These differences are reflected in the size of tissue samples, which are significantly smaller (1mm3), special fixatives, methodology and duration of embedding, different cutting, mounting and coloring of tissue sections...
Author: prof. Dr. I. Tanaskovic

## Slide 3: Sampling for ТЕМ
Taking samples for TEM (by biopsy or necropsy) should be done quickly, avoiding mechanical tissue damage.
A sample of approximately 1x1mm size is taken, which is important for the successful fixation and dehydration of the tissue.

## Slide 4: Tissue processing
The standard tissue fixation protocol for electron microscopy involves prefixation in glutaraldehyde to stabilize proteins, followed by postfixation in osmium tetroxide to preserve lipids.
Tissue processing for TEM takes three days and consists of the following procedures.

## Slide 5
Prefixation is performed in a solution of 2.5% glutaraldehyde in 0.1 M cacodylate buffer (pH 7.4), overnight at a temperature of 4ºC.
Postfixation is performed in a 1% OsO4 solution in 0.1 M cacodylate buffer for 1 hour at 4ºC, after which the samples are left overnight in a saturated solution of 4.8% uranyl acetate at 4˚C.
Dehydration follows in ascending order of alcohol and
Embedding in epon (Epoxy resin).
Samples are cut on an ultramicrotome.
Semi-thin sections used for light orientation microscope, they are most often stained with toluidine blue.
Ultrathin sections are stained with a 2% solution of uranyl acetate and lead citrate.

## Slide 6: Tissue fixation for TEM
Tissue fixation for transmission electron microscopy is most often performed in a solution made of 3% glutaraldehyde in 0.1 M cacodylate buffer overnight or up to 7 days, at 4°C.
The fixative is made from 2.5ml of 0.4M cacodylate, 1.25ml of 25% glutaraldehyde and water is added to 10ml.
https://www.bio-world.com/elisa- buffer/sodium-cacodylate-buffer-02m-ph-74-p- 40120084

## Slide 7
Cacodylate buffer is made by mixing 4.28 g of sodium cacodylate in 100 ml of deionized and distilled water, which results in a 0.2M solution of sodium cacodylate.
Then 5.5 ml of 0.2 N HCl (pH = 7.4) is added to this solution.
It can also be used for the same purpose commercially available solution.

## Slide 8: Tissue processing for TEM
The fixed tissue was washed in 0.1M cacodylate buffer (pH = 7.4) three times for 10 minutes at room temperature.
Then the tissue sample is immersed in a solution obtained by dissolving 1% OsO4 in 0.1M cacodylate for 1 hour at 4°C.

## Slide 9
The fixed tissue was washed in 0.1M cacodylate buffer (pH = 7.4) three times for 10 minutes at room temperature.
Then the tissue sample is immersed in a solution obtained by dissolving 1% OsO4 in 0.1M cacodylate for 1 hour at 4°C.

## Slide 10: Embedding for TEM – DAY 1
After that, a 1:1 solution of 2% aqueous OsO4 and 0.2M cacodylate is prepared.
The resulting solution is pipetted into sample vials, and then washed in 0.1M cacodylate buffer (pH= 7.4) three times for 10 minutes at room temperature.
The tissue is then placed in 4.8% uranyl acetate to stand overnight at 4°C.

## Slide 11: Embedding for TEM – DAY 2
The procedure begins with washing the tissue, first for 5 minutes in water at room temperature, and then for 5 minutes in 50% ethanol at 4°C, which achieves better preservation of cytological details.
This is followed by dehydration in 70% and then 95% ethanol (both for 30 minutes at 4°C) and finally in 100% ethanol three times for 10 minutes at room temperature.
Clesring in propylene oxide three times for 10 minutes at room temperature follows.
The samples are then placed in the mixture complete epon and propylene oxide in a ratio of 1:1. over night.

## Slide 12: Embedding for TEM – DAY 3
The tissue is immersed in a mixture of Epon: Propylene oxide in a ratio of 3:1.
This is followed by embedding in Epon (Epoxy resin), which consists of:
  Epona 812 (4.8ml)
  DDSA (1.7ml)
  MNA (3.5ml)
  DMP-30 (0.2ml)

## Slide 13: Sectioning for ТЕМ
The tissue blocks are cut with a diamond knife on an ultramicrotome.
Usually, the so-called "semi-thin" sections (0.5 - 1 μm) which are stained with toluidine blue for orientation on the light microscope.

## Slide 15
Semi-thin section (for orientation on the light microscope), on the basis of which ultrathin sections are cut for TEM (toluidine blue, x 128; Tanasković I).

## Slide 16
After orientation on the light microscope, ultra-thin sections are cut from a precisely defined part of the block, "caught" on meshes, and then colored - contrasted with heavy metal salts: 2% uranyl acetate and lead-citrate.

## Slide 17
Ultrathin sections are up to 100nm thick (most often 50-80nm).
The grids have a diameter of 3.05 mm, the thickness and size of the "eyes" from just a few to 100 μm (they can be made of copper, molybdenum, gold or platinum)

## Slide 18
Uranyl acetate and lead citrate scatter electrons well.
It is not necessary to release Epon from the preparation in order to contrast the sample.
The excess "color" is washed off and after drying it is observed on a TEM.

## Slide 19: Observation on TEM
The prepared meshes are placed on the support and put in transmission electron microscope.
In TEM, the source of visualization is a directed beam of electrons (instead of photons, as is the case with a light microscope).
https://www.nottingham.ac.uk/nmrc-commercial/nmcs-facilities/tem.aspx

## Slide 20
The TEM has condenser and objective lenses.
Condenser lenses (electromagnetic coils) by means of the magnetic field focus the electron beam emitted from the electron gun (tungsten filament) in a high vacuum.
https://www.nottingham.ac.uk/nmrc-commercial/nmcs-facilities/tem.aspx

## Slide 21
Objective lenses represent an image creation system that is eyepiece equivalent (exists instead of eyepiece)
These are projector lenses that form an image on a flat metal plate coated with fluorescent material or on a screen.
https://www.nottingham.ac.uk/nmrc-commercial/nmcs-facilities/tem.aspx

## Slide 22
Condenser lenses (electromagnetic coils) use a magnetic field to focus a beam of electrons emitted from an electron gun (tungsten filament) in a high vacuum.
Objective lenses are an image-forming system that is equivalent to an eyepiece (it exists instead of an eyepiece).
These are projector lenses that form an image on a flat metal plate coated with a fluorescent material or screen.

## Slide 23
A directed beam of electrons passes through the sample and changes the density due to the structure of the sample.
When they hit the image capturing device, the glow is stronger where there are many electrons and that place is bright or vice versa.
In this way, the image created on the screen is a true reflection of the object being observed because it reflects differences in density different parts of the sample.
https://vaccoat.com/blog/electron-microscope/

## Slide 24
Capillary in the adventitia of the aorta (TEM, x 8250) prof. Dr. Irena Tanasković
Smooth muscle cell of synthetic phenotype (TEM, x 17500) prof. Dr. Irena Tanasković

## Slide 25
Foam cell (TEM, x 16750) prof. Dr. Irena Tanasković
Apoptosis (TEM, x 17500) prof. Dr. Irena Tanasković

## Slide 26
Collagen fibers (TEM, x 17500) prof. Dr. Irena Tanasković
Necrosis (TEM, x 17500) prof. Dr. Irena Tanasković

## Slide 27: Scanning electron microscopy (SЕМ)

## Slide 28: Tissue processing for SЕМ
The samples are prepared by immersing in an ultrasonic bath containing distilled water for 20 minutes.
After that, the samples are dried at a temperature of 37ºC for 24 hours.
This is followed by dehydration in increasing concentrations of ethanol for 20 minutes each, which ends immersion in 100% ethanol for 1 h.
Samples are placed on aluminum supports using a special adhesive tape.

## Slide 29
Preparation of samples is carried out in under vacuum conditions.
The samples are brought to a special apparatus
They "steam" with 20 nm thick gold for 100 s at a current of 33 mA.
A thin film of heavy metal (platinum, gold), is steamed at an oblique angle so that in some places more and in others less remains ("shading").
A replica of the sample is placed on the surface of a strong solvent as would dissolve the sample.
The replica is then rinsed and placed to the copper grid for testing.

## Slide 30
Scanning electron microscope (JEOL-JSM-661 OLV, Tokyo, Japan)
Faculty of Mining and Geology of the University of Belgrade (photo from the PhD dissertation of Dr. Diana Nogo - Živanović, mentorship: prof. Dr. Irena Tanasković)

## Slide 31
These microscopes allow examination of surface structures, because they create three-dimensional image of the object.
At the top of the device is a source of electrons, a thin tungsten filament.
The electron beam is not static, but moves across the sample (scans it).
When the electrons hit the sample, with secondary electrons are released from a given place, which scatter from that place in a direction that depends on the angle of the incident beam and the topography of the sample surface
.

## Slide 33: Скенирајући електронски микроскоп
Photomicrography: Blue Histology
http://www.lab.anhb.uwa.edu.au/